## Slide 1: Tires
“Secrets to Success”
- Unit 6 -

## Slide 2: In the bad old days…

## Slide 3: In the really bad really old days

## Slide 4: And the confused days…

## Slide 5: Pneumatic Tires
Dunlop patented them for bicycles in 1888
Michelin put them on cars in 1895
Goodyear was started in 1898. Named after the inventor of vulcanized rubber.

## Slide 6: Inner tube tires
Tires with inner tubes were used until the 50s. Inner tubes have a few benefits.

## Slide 7: How to fill up a Tire?
Dunlop patented them for bicycles in 1888

## Slide 8: What should your tire pressure be?
Max inflation on the side of the tire
Manufacturer suggested pressure on the door pillar tag.
Overinflation gets better fuel mileage
Underinflation gets slightly better ride and better off-road traction
Check when ambient temperature

## Slide 9: N2? What’s with the green caps?
Benefits?
Side effects?
Cost Effective?

## Slide 10: Bias-ply tires
Had plies of cords that ran at 55 degree angles to the rim.
Pliable, but lots of rolling resistance.
Tire Designs

## Slide 11: Radials
Introduced in 1948 by Michelin
Americans resisted until the 70s
By 1982, all cars sold in the US had steel belted radials
Tire Designs

## Slide 12: Tire Construction

## Slide 13: Sidewall construction
Sidewalls hold the tire up
More plies:
Carry more load,
less side to side
movement
Less plies: Softer ride

## Slide 14: Tread design
Which tire has the best traction?
A B C

## Slide 15: Tread characteristics
More rubber to the ground means more friction
Too much rubber on the ground leaves no room for water to escape
Small voids pack full of snow and mud
Large voids squirm and howl

## Slide 16: Tread composition
Soft tread
sticks better
Hard tread
lasts longer
Hot vs. Cold

## Slide 17: UTQGS Tread codes Uniform Tire Quality Grading Standards
Traction – A B C
Straight ahead traction on a wet surface
Temperature – A B C
Represent a tire’s ability to withstand heat
Treadwear – between 60- 620
Tires are tested in controlled conditions on a government test track.
For comparison purposes. The numbers don’t mean anything

## Slide 18: Tire Sizes
Old time codes
70D
Sizes in inches
35X12.5X15
P-metric codes
P185/75R15

## Slide 19: Old time tire with code

## Slide 20: Inch size tire

## Slide 22: Tire Classifications
Tread Design
  M + S
  Snow
Tire Sizes

## Slide 23: Snow tires in action?
RWL – Raised white lettering
OWL – Outline white lettering
White wall vs. black wall
M&S – Mud and Snow

## Slide 24: Tire Classifications
Tire Plies
Tire Grading
  Treadwear
  Traction
  Temperature

## Slide 25: Tire Classifications
Run Flat Tires
  Self-sealing
  Self-supporting
  Tire/wheel combination
  systems

## Slide 26: Tire Care and Maintenance
Tire Wear Indicator Bars
  Set at 2/32nds of an inch (1.6 mm)

## Slide 27: Wear bars
Tires can use bars or dots to indicate wear

## Slide 28: Tire Care and Maintenance
Torque lug nuts in a star pattern

## Slide 29: Tire Care and Maintenance
Tire Repairs
  Use a patch/plug combination – requires removal of tire from wheel
  Do not repair sidewalls
Tire Pressure Monitoring System
  Monitors tire pressure
  Required on vehicles built on or after Sept 1st, 2007

## Slide 30: Tire Care and Maintenance
Always refer to the tire placard for tire pressure information

## Slide 31: Review questions
Q. What does a Traction rating of “B” mean?
A. it is the middle grade for straight ahead wet traction
Q. What is a M&S tire good for?
A. Mud and Snow
Q. What does 305/80R16 mean?
305 mm wide/ 80% tall Radial 16” rim

## Slide 32: More review questions
Q. What tread design helps in ice?
A. siping
Q. What is the measurement of a bald tire?
A. 2/32” or less
Q. What is hydroplaning?
A. Water trapped under the tire lifts the tire off the road.

## Slide 33: Why do tires wear?
Cornering forces
Driving forces
Misalignment
Bad steering parts
Bad shocks
Scuffing
Skidding

## Slide 34: Cornering forces

## Slide 35: Driving forces

## Slide 36: Misalignment

## Slide 37: Bad steering parts

## Slide 38: Bad shocks

## Slide 39: scuffing

## Slide 40: Skidding

## Slide 41: Overinflation

## Slide 42: Underinflation

## Slide 43: Tire Care and Maintenance
Tire wear

## Slide 44: How can you make your tires last longer?

## Slide 45: Rotate your tires

## Slide 46: Tire Rotation patterns
The average tires should be rotated every 10K miles
RWD AWD / 4WD FWD Directional

## Slide 47: Do not over inflate your tire! Check with your owners manual or B-pillar

## Slide 48: Lets see how it’s made!
Tires: How its made

## Slide 49: The future of tires?
Secrets to success

## Slide 50: Tire Machine
Secrets to Success